## Slide 1: Board of Selectmen Meeting
Central Street Improvements
MassDOT Project No. 608548
Monday, October 30, 2017
Presenters:
David L. Loring, P.E., ENV SP, LEED AP
Vice President, Tighe & Bond
Alexander D. Fagnand, P.E., ENV SP
Project Engineer, Tighe & Bond
Notes: DLL

## Slide 2: Project Description
Project Length – 2,600 Feet
  Front Street to Maple Street (not including Blair Square)
Scope of Work ($3.5m – $3.75m)
  Full Depth Roadway Reconstruction & Storm Drainage
  Enhanced Pedestrian and Bicycle Accommodations
  Streetscape Amenities
  Municipal Sanitary Sewer & Water Main Replacement (non-participating local cost)
Funding Sources
  FHWA Transportation Improvement Program (TIP) administered by MassDOT ($2.75m)
  Local contribution for municipal utilities (approx. $750k - $1m)
Notes: DLL

## Slide 3: Locus Plan
Notes: DLL

## Slide 4: Existing Conditions
Roadway Characteristics
  50-60’ Right of Way
  Travel Lanes (2); Parking Lanes (2); Sidewalks (2)
  Gentle grades
  25 MPH Speed Limit
  8,900 Vehicles per Day (ADT)
Pavement
  Failing due to age, weak subbase, and poor drainage
  Potholes; longitudinal cracks; alligator cracks
  Utility trench repair patches
Utilities
  Existing utilities are old and undersized
  Recent repairs due to failures
Notes: ADF

## Slide 5: Corridor Deficiencies
Safety
  High accident rate
    State Average crash rate: 3.70 MEV
    Central Street crash rate: 8.47 MEV
  Intersection sight distance (ISD)
  Dangerous pedestrian crossings
Multi-modal & ADA accommodations
  Poor sidewalk condition; inadequate curb cut ramps
  No dedicated bicycle space
Streetscape
  Effective and aesthetic lighting
  Plantings and street furniture
  “Livable” space
Notes: ADF
Biggest accident clusters at Summer & Grove

## Slide 6: Typical Deficiencies
Intersection Sight Distance
ADA Compliance
Notes: ADF

## Slide 7: Public Input
Central Street Improvements Survey (Residents)
  Conducted in person at 2017 Fall Fest with survey cards
  Conducted online using Survey Monkey
  32 responses
Town Meeting (Town Officials)
  Presentation to Select Board and Planning Board
Continued Stakeholder Conversations
  Local business owners
  Direct project abutters
  Regional Chamber of Commerce
Notes: ADF

## Slide 8: Survey Results
Why do you visit Central Street?
Chart: Reason for Trip
| Food | Errands/Appointments | Community/Social | Recreation
Responses | 23 | 22 | 13 | 10
Notes: ADF

## Slide 9: Survey Results
What improvements would encourage you to visit more often?
Chart: DESIRED AMENITIES
| Bus Shelter | Bike Rack | Benches | Parking | Trees & Plantings
 | 4 | 4 | 23 | 10 | 18
Notes: ADF

## Slide 10: Survey Results
Please rank the following roadway improvements from 1 (most important) to 5.
Pedestrian
Parking
Bicycle
Landscaping
Bus
1
5
Notes: ADF
1 – Pedestrian (3.72)
2 – Parking (3.25)
3 – Bicycle (3.17)
4 – Landscaping (3.04)
5 – Bus (1.83)

## Slide 11: Survey Results
Speeding
  “Currently, traffic moves too fast down Central Street…”
  “Speeding. Central Street is thickly settled – 25 mph…”
Streetscape
  “…plants plants plants…”
  “Need to somehow tie each end of Central Street together…”
  “Park benches. Better sidewalks. Outside dining…”
Blair Square
  “Need rotary”
  “A rotary at Central and Front…”
  “…a traffic light at the intersection of Route 12…”
Notes: ADF

## Slide 12: Road Design
Engineering Practice & Principles
Review of pertinent guidance (State & Federal)
Application of engineering principles
Funding Program Requirements (TIP)
MassDOT project delivery & design review
Relevant Local Policies
Complete Streets Policy
Planned Development Relevant Local Policies
Local Stakeholder Input
Project Proponents (Planning & Development; DPW)
Town Officials (Select Board & Planning Board)
Residents & Local Business Owners
Notes: ADF

## Slide 13: Road Design
Multi-modal Roadway Section
  Travel lanes (2); Bicycle Lanes (2); Parking Lane (1); Sidewalks (2)
  Parking lane on western side of the road
    Adjacent to commercial store fronts
    Eastern side has more off-street parking
  Room for streetscape amenities
Notes: ADF
“Parking Compromise”
Reduction in on street parking for
1. Safety improvements (ISD)
2. Multi-modal accommodations
3. Streetscape amenities
Mitigation of parking loss
Existing abundance of on-street parking
Additional off-street and side street parking
New short-term parking regulations

## Slide 14: Next Steps
10% Design – November 2017
  Finalize the FDR and meet with MassDOT
25% Design – January 2018
  Preliminary Design to MassDOT & Design Public Hearing
75% Design – June 2018
  Revised Design & Environmental/Land Use Permits
100% / PSE Design – December 2018
  Revised Design & Construction Documents
Construction in Spring 2020
10% Design
(November ‘17)
25% Design
(January ‘18)
75% Design
(June ‘18)
100% / PSE Design
(December ‘18)
Construction
(Spring 2020)
Notes: DLL

## Slide 15: Summary
Opportunity to address Central Street Deficiencies
Accepting TIP funds means the Town must comply with MassDOT/FHWA design standards
Draw people back to downtown; spur on economic development
Downtown Complete Streets projects result in economic returns
  Park Street in Adams
  North Elm, Elm, and Main Street in Westfield
Notes: DLL
Deficiencies (utilities, pedestrian, bicycle, safety, roadway)
Drawbacks (limited control of design process, conformance to state & national standards)
Benefits: leverage funding to improve corridor with utility improvements & economic growth